## Slide 1
A
Project
by
Jahnavi Tejomurtula
Ashmita Chakraborty
Abhash Malviya
Abhilash Naredla
Department of Electrical Engineering
DEVELOPMENT OF MULTI-LAYERED DATA CENTER ARCHITECTURES
USING
SOFTWARE DEFINED NETWORKING
Under the guidance of
Prof. Dr. Nader F Mir

## Slide 2
INTRODUCTION
Need for Data Center Network
Increased need for data availability and better performance
To Enable large storage domain and faster network switching
What is a Data Center Network
Need for a Scalable network
Need for a Software defined Control
A collection of storage and network devices connected over a communication channel
A Network which provides a virtualized environment
Maximizing flexibility, increasing design life cycle
Decreasing cost of the network and latency
Increased processing delays, physical switching requirements due to control and data operating in parallel
Software Defined Networking
Decoupled control logic from data plane which shifts the control on network to a centralized controller
Decreases the physical management costs and improves operational flexibility

## Slide 3: INTRODUCTION
SJSU Washington Square
Multi-Tier Architecture
Fat tree Architecture

## Slide 4
INTRODUCTION: PROGRAM FLOW & TOOLS
TOOLS USED
IPERF- BANDWIDTH CALCULATION
Mininet> iperf <Source Host Name> <Destination Host Name>
*** Iperf: testing TCP bandwidth between <Source Host Name> and <Destination Host Name>
*** Results: ['1.69 Gbits/sec', '1.70 Gbits/sec']
PINGALLFULL-DELAY CALCULATION
Mininet> pingallfull
Mininet- SDN Simulator
Ovs-vsctl – Open VSwitch Command Line
Python API
PROGRAM FLOW

## Slide 5: FAT TREE ARCHITECTURES
ton Square
16 Host Architecture: 4 Racks and 4 Hosts per Rack
Layered Architecture
Non-Layered Architecture
Chart: Average Bandwidth-Average Delay for Inter Rack and Intra Rack Communication
| Non Layered | Layered
Average Bandwidth of Inter Rack 16 Host Architecture | 20.6667 | 8.7
Average Bandwidth of Intra Rack 16 Host Architecture | 26.46 | 24.916
Average Delay of Inter Rack 16 Host Architecture | 7.9733 | 20.58
Average Delay of Intra Rack 16 Host Architecture | 2.485 | 7.18
Chart: Delay -Bandwidth Analysis Between Layered and Non Layered 16 Host Fat Tree Architecture
| Non Layered | Layered
Average Bandwidth | 23.56 | 16.8
Average Delay | 5.22 | 13.88

## Slide 6: FAT TREE ARCHITECTURES
ton Square
35 Host Architecture: 5 Racks and 7 Hosts per Rack
Layered Architecture
Non-Layered Architecture
Chart: Average Delay- Average Bandwidth Analysis for Inter Rack and Intra Rack Communication
| Non Layered | Layered
Average Bandwidth of Inter Rack 35 Host Architecture | 3.2065 | 6.8114
Average Bandwidth of Intra Rack 35 Host Architecture | 4.73 | 5.5475
Average Delay of Inter Rack 35 Host Architecture | 28.2014 | 43.1526
Average Delay of Intra Rack 35 Host Architecture | 59.0138 | 74.6691
Chart: Delay Bandwidth Analysis Between Layered and Non-Layered 35 Host Fat Tree Architecture
| Non Layered Topology | Layered Topology
Average Bandwidth | 3.96 | 6.17
Average Delay | 20.09 | 32.48

## Slide 7: FAT TREE ARCHITECTURES
ton Square
64 Host Architecture: 6 Racks and 8 Hosts per Rack
Layered Architecture
Non-Layered Architecture
Chart: Average Bandwidth-Average Delay for Inter Rack and Intra Rack Communication
| Non Layered | Layered
Average Bandwidth of Inter Rack 64 Host Architecture | 4.093 | 3.1388
Average Bandwidth of Intra Rack 64 Host Architecture | 4.7076 | 3.7542
Average Delay of Inter Rack 64 Host Architecture | 46.6157 | 59.3459
Average Delay of Intra Rack 64 Host Architecture | 22.3024 | 31.67
Chart: Delay Bandwidth Analysis Between Layered and Non-Layered 64 Host Fat Tree Architecture
| Non Layered | Layered
Average Bandwidth | 4.4 | 3.44
Average Delay | 34.45 | 45.5

## Slide 8: FAT TREE ARCHITECTURES
ton Square
98 Host Architecture: 7 Racks and 14 Hosts per Rack
Layered Architecture
Non-Layered Architecture
Chart: Average Delay- Average Bandwidth Analysisfor Inter Rack and Intra Rack Communication
| Non Layered | Layered
Average Bandwidth of Inter Rack 98 Host Architecture | 4.1195 | 3.6465
Average Bandwidth of Intra Rack 98 Host Architecture | 5.0841 | 4.9715
Average Delay of Inter Rack 98 Host Architecture | 27.29 | 44.24
Average Delay of Intra Rack 98 Host Architecture | 12.9 | 20.73
Chart: Delay Bandwidth Analysis Between Layered and Non Layered 98 Hots Fat Tree Architecture
| Non Layered | Layered
Average Bandwidth | 4.6 | 4.3
Average Delay | 20.09 | 32.48

## Slide 9: FAT TREE ARCHITECTURES
ton Square
Overall Delay- Bandwidth Analysis of Fat-Tree Architectures
Chart: Delay Analysis for Fat Tree Layered and Non Layered Architecture
| 16 Host | 35 Host | 64 Host | 98 Host | 16 Host | 35 Host | 64 Host | 98 Host | Layered | Non-Layered
Fat Tree Architectures | 13.88 | 58.91 | 45.5 | 32.48 | 5.22 | 43.6 | 34.54 | 20.09
Chart: Bandwidth Analysis for Layered and Non Layered Fat Tree Architectures
| 16 Host | 35 Host | 64 Host | 98 Host | 16 Host | 35 Host | 64 Host | 98 Host | Layered | Non-Layered
Fat Tree Architectures | 16.8 | 6.17 | 3.44 | 4.3 | 23.56 | 3.96 | 4.4 | 4.6
Chart: Average Delay Analysis for Layered and Non Layered DCN Architectures
| Non Layered | Layered
Hosts from Different Racks | 27.5201 | 41.8296
Hosts from Same Racks | 24.1753 | 33.5623
Chart: Average Bandwidth Analysis for Layered and Non Layered DCN Architectures
| Non Layered | Layered
Inter Rack | 8.0214 | 5.5742
Intra Rack | 10.2454 | 9.7973

## Slide 10: FAT TREE ARCHITECTURES
ton Square
Quantitative Analysis for Fat Tree Architecture
IO Data Analysis Using Wireshark
Chart: Average Throughput in Fat Tree Architectures
| 16 Host Non- Layered | 16 Host Layered | 35 Host Non- Layered | 35 Host Layered | 64 Host Non- Layered | 64 Host Layered | 98 Host Non- Layered | 98 Host Layered
Throughput (Average Packets per Second) | 1343 | 914 | 1626 | 2207 | 2974 | 2337 | 2877 | 1781
Column1
Column2
Throughput Analysis Using Wireshark
Traceroute from Mininet
Pingallfull from Mininet

## Slide 11: MULTI-TIER ARCHITECTURES
Architecture with 16 Hosts; 4 Racks and 4 Hosts per rack
16 Hosts Non-Layered
16 Hosts Layered
Chart: Delay-Bandwidth comparison between Layered and Non-Layered architecture
| Average Bandwidth | Average Delay | Average Bandwidth | Average Delay | Layered | Non-Layered
 | 21.2 | 1.6 | 23.9 | 5.6
Chart: Average Delay-Bandwidth analysis between Inter-rack vs Intra-rack
| Layered | Non-Layered
Average Bandwidth of Intra Rack | 27.63 | 34.14
Average Bandwidth of Inter Rack | 20.1 | 8.34
Average Delay of Intra Rack | 2.9 | 1.83
Average Delay of Inter Rack | 8.28 | 1.33

## Slide 12: MULTI-TIER ARCHITECTURES
Architecture with 32 Hosts; 4 Racks and 8 Hosts per rack
32 Hosts Non-Layered
32 Hosts Layered
Chart: Average Delay-Bandwidth analysis between Inter-rack vs Intra-rack
| Layered | Non-Layered
Average Bandwidth of Intra Rack | 9.69 | 10.63
Average Bandwidth of Inter Rack | 20.05 | 27.07
Average Delay of Intra Rack | 97.8 | 14.54
Average Delay of Inter Rack | 47.39 | 21.94
Chart: Delay-Bandwidth comparison between Layered and Non-Layered architecture
| Average Bandwidth | Average Delay | Average Bandwidth | Average Delay | Layered | Non-Layered
 | 14.9 | 72.6 | 18.9 | 18.2

## Slide 13: MULTI-TIER ARCHITECTURES
Architecture with 64 Hosts; 8 Racks and 8 Hosts per rack
64 Hosts Non-Layered
64 Hosts Layered
Chart: Average Delay-Bandwidth analysis between Inter-rack vs Intra-rack
| Layered | Non-Layered
Average Bandwidth of Intra Rack | 26.18 | 13.55
Average Bandwidth of Inter Rack | 20.59 | 11.37
Average Delay of Intra Rack | 34.48 | 38.43
Average Delay of Inter Rack | 68.49 | 41.13
Chart: Delay-Bandwidth comparison between Layered and Non-Layered architecture
| Average Bandwidth | Average Delay | Average Bandwidth | Average Delay | Layered | Non-Layered
 | 23.4 | 51.5 | 12.5 | 39.8

## Slide 14: MULTI-TIER ARCHITECTURES
Architecture with 96 Hosts; 2 Racks with 48 servers and 6 racks with 16 servers each
96 Hosts Horizontally Scaled
96 Hosts Vertically Scaled
Chart: Average Delay-Bandwidth analysis between Inter-rack vs Intra-rack
| Layered | Non-Layered
Average Bandwidth of Intra Rack | 29.14 | 16.65
Average Bandwidth of Inter Rack | 27.47 | 20.17
Average Delay of Intra Rack | 40.84 | 89.68
Average Delay of Inter Rack | 43.96 | 86.45
Chart: Delay-Bandwidth comparison between Layered and Non-Layered architecture
| Average Bandwidth | Average Delay | Average Bandwidth | Average Delay | Layered | Non-Layered
 | 28.3 | 42.4 | 18.4 | 88.1

## Slide 15: Overall Delay-Bandwidth analysis Multi-Tier architecture
SJSU Washington Square
Chart: Bandwidth analysis of different topologies
| 16 | 32 | 64 | 96
Average Bandwidth Layered | 21.2 | 14.9 | 23.4 | 28.3
Average Bandwidth Non-Layered | 23.9 | 18.9 | 12.5 | 18.4
Chart: Delay analysis of different topologies
| 16 | 32 | 64 | 96
Average Delay Layered | 1.6 | 72.6 | 51.5 | 42.4
Average Delay Non-Layered | 5.6 | 18.2 | 39.8 | 88.1
MULTI-TIER ARCHITECTURES

## Slide 16: MULTI-TIER ARCHITECTURES
Quantitative Analysis
IO Data Analysis using Wireshark
Chart: Average Throughput of Multi-Tier Architecture
| 16 Hosts | 32 Hosts | 64 Hosts | 96 Hosts
Average Throughput | 2027.5 | 4648.2 | 13346.8 | 6321.9
Packet inspection using Mininet commands; Link, Switch and Traceroute

## Slide 17: COMPARATIVE ANALYSIS FOR FAT-TREE AND MULTI-TIERED ARCHITECTURE
ton Square
16 Host Core-Host Communication: Fat Tree Architecture
16 Host Core-Host Communication: Multi-Tiered Architecture

## Slide 18: COMPARATIVE ANALYSIS FOR FAT-TREE AND MULTI-TIERED ARCHITECTURE
ton Square
Chart: Delay Analysis for Fat Tree and Multi-tiered topologies
| 16 Host | 35 Host | 64 Host | 98 Host | 16 Host | 35 Host | 64 Host | 98 Host | Layered | Non-Layered
Fat Tree Architectures | 13.88 | 58.91 | 45.5 | 32.48 | 5.22 | 43.6 | 34.54 | 20.09
Multi-tiered Architectures | 1.6 | 72.6 | 51.5 | 42.4 | 5.6 | 18.2 | 39.8 | 88.1
Chart: Bandwidth Analysis for Fat Tree and Multi-tiered Topologies
| 16 Host | 35 Host | 64 Host | 98 Host | 16 Host | 35 Host | 64 Host | 98 Host | Layered | Non-Layered
Fat Tree Architectures | 16.8 | 6.17 | 3.44 | 4.3 | 23.56 | 3.96 | 4.4 | 4.6
Multi-tiered Architectures | 21.2 | 14.9 | 23.4 | 28.3 | 23.9 | 18.9 | 12.5 | 18.4
Average Delay and Average Bandwidth Comparison of Fat Tree and Multi-tiered Architectures

## Slide 19
CONCLUSION
Multi-Tier Architecture
Offers better Bandwidth when vertically scaled
Higher Average Delay
Fat-Tree Architecture
Offers lower delay
Increased number of switches increases network complexity
Offers less bandwidth when scaled
Multi-Tier Architecture is better suited for vertical scaling

## Slide 20
REFERENCES
Software Defined Networks (EWSDN), 2013 Second European Workshop on, Issue Date: 10-11 Oct. 2013, Written by: Teixeira, J.; Antichi, G.; Adami, D.; Del Chiaro, A.; Giordano, S.; Santos, A.
M. Al-Fares, A. Loukissas, and A. Vahdat, ``A scalable, commodity datacenter network architecture,'' in Proc. ACM SIGCOMM, 2008, pp. 63_74.
T. Lam et al., ``NetShare: Virtualizing data center networks across ser-vices,'' Dept. Comput. Sci. Eng., Univ. California, Berkeley, CA, USA, Tech. Rep., 2010.
TING WANG1, (Student Member, IEEE), ZHIYANG SU1 , (Student Member, IEEE), YU XIA1 , (Member, IEEE), AND MOUNIR HAMDI1,2 , (Fellow, IEEE) Department of Computer Science and Engineering, The Hong Kong University of Science and Technology, Hamad Bin Khalifa University, Doha, Qatar “ Rethinking the Data Center Networking:Architecture, Network Protocols and Resource Sharing “, 2013